## Slide 1
ESP_012860_1830 Aram Chaos
MRO, especially HiRISE
Alfred McEwen
ESP_014339_0930
S. Pole residual cap in mid-summer

## Slide 2: JOURNAL OF GEOPHYSICAL RESEARCH, VOL. 112, E05S01, 2007 An overview of the Mars Reconnaissance Orbiter (MRO) science mission Richard W. Zurek and Suzanne E. Smrekar
Top-level science objectives of the Mars Exploration Program:
  1. Search for evidence of past or present life.
  2. Understand the climate and volatile history of Mars.
  3. Understand geological processes and their role in shaping the surface and subsurface.
  4. Assess the nature and inventory of resources on Mars in preparation for human exploration.
MRO mission objectives:
  Present Climate
1. Observe seasonal cycles and daily variations of water, dust and carbon dioxide on Mars.
2. Characterize Mars’ global atmospheric structure, atmospheric circulation, and surface changes…
  Aqueous Activity
    Investigate local areas for compositional evidence of such environments, and in particular the presence of surface materials conducive to biological activity or having the potential for preserving biogenic materials.
    Observe and quantify the detailed stratigraphy and geomorphology of key locales in order to identify formation processes of geologic features indicating the presence and persistence of liquid water.
    Probe the horizontal and vertical structure of the uppermost surficial layer on Mars and its potential reser- voirs of water and water ice.
  Geosciences
  1. Map and characterize in detail the stratigraphy, geomorphology, and composition of the Mars surface and subsurface at many globally distributed locales to understand better the nature and evolution of different Martian terrain types.
  2. Characterize the Martian gravity field in greater detail to improve knowledge of the Martian crust and lithosphere and of atmospheric mass variation.
  Mission Support:
  Relay from landed missions
  Landing sites characterization and certification

## Slide 4
Radar sounding
SHARAD

## Slide 5: MRO Orbit
Sun-synchronous ~3 AM/PM (why that time of day?)
250-320 km altitude (why?)
Inclination 92.65 deg. (why?)
12.8 orbits/day
Nadir pointed, roll cross-track up to 30° (what does that enable?)

## Slide 6: Data Return Comparison (MRO now >600 Tb)
2026 Update: HiRISE has returned >195 Tbits of Mars data

## Slide 7: MRO Mission Overview
Launch
Interplanetary Cruise
Approach and Orbit Insertion
Aerobraking
Primary Science/Relay
Aug 2005
Mar-Sep 2006
Aug 2005 - Mar 2006
Nov 2006 - Dec 2010
Mar 2006
LC-41
Atlas V-401
Capture Orbit ---
Period: 35 hrs
Asc Node: 8:30 pm LMST
Science Data
Acquisition/Return
Primary Science/Relay Orbit ---
Period: 112 min
Hp: 255 km Ha: 320 km, Frozen
Ascending Node: 3:00 pm LMST (Sun-Sync)

## Slide 9
MRO in Thermal-Vacuum Chamber
Sign on cover: “REMOVE BEFORE FLIGHT”

## Slide 10
First-light image from HiRISE

## Slide 11: Transport to Kennedy Space Center (KSC) on Air Force C17 cargo Plane

## Slide 13: Aug 12, 2005: Launch!

## Slide 14: Mars Orbit Insertion March 10, 2006

## Slide 15
SHARAD
MARCI
CTX
CRISM
MCS
MRO Science Instruments
HiRISE

## Slide 16: How to take images from an orbiter
Framing (like your cell phones, and Viking Orbiter cameras)
Pushbroom
  CTX – single line moves across surface for s/c motion
  HiRISE – same, but multiple lines (TDI) and detectors
  CRISM – can use gimbals to slow rate of motion over surface, to increase exposure time
Scanner--MCS – scanner—set of “single pixel” detectors scan up and down along with s/c motion (like Landsat MSS)
Radar sounding -- SHARAD
Push-frame--MARCI (see animation), also CaSSIS on TGO

## Slide 17: Context Imager (CTX)
Simple B&W line array, 5-6 m/pixel
Has now covered >99% of Mars!

## Slide 20
CRISM FRT 58A3 Draped on CTX
From Ralph Milliken
Minerals in Gale Crater

## Slide 22
HiRISE Coverage as of 10/7/2013

## Slide 23: HiRISE Camera Designed, Integrated, and Tested at Ball Aerospace & Tech. Corp.
Remote Electronics
Power
Supply
Focal Plane
Electronics
Metering Structure
Baffle
Tube
Sunshade
Spacecraft Structure
Support ring ~1 m diameter

## Slide 24: HiRISE Ray Trace
Tertiary Mirror
Secondary Mirror
Secondary Mirror Baffle
Primary Mirror
Primary Mirror Baffle
Focus
Mechanism
2nd Fold
Mirror
1st Fold
Mirror
Filters
Focal
Plane
Focal Plane
Electronics

## Slide 25: Installing the Primary Mirror

## Slide 26: HiRISE Focal Plane Assembly
14 CCDs (2048 x 128 pixels):
  10 CCDs Form Red Channel (20,000 pixels)
  2 CCDs Form Blue-Green Channel (4000 pixels)
  2 CCDs Form NIR Channel (4000 pixels)
Notes: 14 CCDs staggered

## Slide 27: TDI (Time Delay and Integration) Increases Signal
3
4
1
2

## Slide 28: Biggest Instrument Challenge: Speed!
HiRISE field-of-view moves over the surface of Mars at 3.2 km/s (~7,000 miles per hour)
Must collect and store the equivalent of 1000 1-megapixel images in ~6 seconds!
This is analogous to imaging coarse sand grains on the road while driving 125 miles/hour!

## Slide 29
  S/C orbital motion (Nadir) “pushes” sensor projection across ground
  Line integration timing is identically matched to orbital ground speed (~3.2 km/s or 6,912 mph!)
  25-32 cm/pixel
  Sensor (linear array of pixels) integrates during motion of single pixel: ~0.0001 second!
Altitude varies with latitude and topography, ~250-315 km
2048 x128 TDI Line Arrays
Color Filters suspended above each detector
Flexible band tuning
Multiple colors
HiRISE FPA
20,000 pixels (non-overlap) in Cross-Track direction
IFOV = 1.0 µrad
FOV = 1.15 degrees (20K pixels)
“Swath Width”
Sub-satellite (nadir) velocity direction
50 cm aperture, F/24 (HiRISE Optical System)
Color Swath Width
Image Length
Sub-satellite (nadir) velocity
HiRISE “Pushbroom” Imaging
High resolution Imaging Science Experiment, Alfred McEwen, PI

## Slide 30: HiRISE Images with color stripe and full-res sample

## Slide 31: Stereo Data Acquisition on different orbits
Acquire ~1000 stereo pairs in 2 years
Digital Elevation Model (DEM) resolution ~1 m
Require q1+q2 >15° for 0.2 m vertical precision
Left: DEM of part of Columbia Hills (Kirk et al., 2008)
Home Plate

## Slide 32
History of W Candor Chasm, Okubo et al., 2009.

## Slide 33: Mound in Ganges Chasm https://www.flickr.com/photos/136797589@N04/
NO VERTICAL EXAGGERATION

## Slide 34: HiRISE Radiometric Calibrations
Pre-flight cal with in-flight checks (why?)
HiRISE has many image modes for radiometric cal:
  TDI 8, 32, 64, 128
  Pixel binning 1x1, 2x2, 3x3, 4x4, 8x8, 16x16
  14 CCDs
  Sides A and B of remote electronics (and stim lamps)
  Wide range of exposure (line) times
  Need dark frames, flat-field frames, light transfer function, variations with temperature
  Only 1 week to try to measure all of this at Ball Aerospace before delivery for spacecraft integration
  Then we loaded new FPGA code at the launch site!
  Radiometric cal is never done, you just get diminishing returns until nobody (sane) wants to work on it any more

## Slide 35: HiRISE Geometric Calibrations
Pre-flight
  Measure precise positions of CCDs
  Measure optical distortions
In-Flight
  Star cals to tweak optical distortion model
  Measure and correct distortions from pointing jitter
    Esp, important for digital terrain models

## Slide 36
HiRISE at Mars:
Jan 27, 2026
103,247 Mars images returned
55,717 Giga-pixels
  Covers 5.12% of Martian surface (3.5% unique)
  Covers >0.5% in color
8,713 planned stereo pairs completed
  ~0.42% of Mars covered in stereo
  1,216 DTMs produced for PDS archival
ESP_049009_1520

## Slide 37
Opportunity at Victoria Crater
0.5 mile diameter

## Slide 38: Phoenix Descending
Right: after landing and opening solar fans

## Slide 39: MSL crashes stuff on Mars in 2012
Before
After

## Slide 40
25 m
Opportunity rover stuck for 5 weeks in Purgatory cross drifts composed of cohesionless sand. With HiRISE images the rover avoided such areas en route to Endeavour crater.
1/25/26
40
Golombek: Remote Sensing Traverse

## Slide 41: Curiosity Traverse
Wheel damage seen by 2014
MSL team uses HiRISE images to carefully select the path to minimize damage, avoiding the hard sandstone.

## Slide 42
Bull’s-Eye Crater
ESP_018522_2270

## Slide 44: Fault (All images ~1 km wide)

## Slide 45: Fluvial landforms in Melas Chasm

## Slide 46: Subaqueous fans in Melas Chasm

## Slide 47: Folded sedimentary rock layers

## Slide 48: Faulted and tilted layered sediments

## Slide 50: Bedrock patterns in Gale crater

## Slide 51: Dunes in Herschel Crater

## Slide 52: Pedestal crater

## Slide 53: Phreatovolcanic cones

## Slide 54: NW rim of Endeavor Crater

## Slide 55: Dust avalanches, triggered by dust devil?

## Slide 56
Viscous flow

## Slide 57: The Future of HiRISE
MRO has fuel for another 10+ years
HiRISE camera still working but has issues
  One of 14 CCD electronics units failed in 2011, another fails often since 2023
  Increasing noise issues
No way to predict when flight hardware might completely fail

## Slide 58: How to Make HiRISE Image Suggestions
You need to enter at least 3 suggestions by Feb 18!
  Go to https://www.uahirise.org/hiwish/ and register to create an account. (Demo HiWish)
  Make the 3 targets differ in longitude by at least 10 deg. so they don’t conflict with each other. Current season is late southern spring, so don’t enter targets north of latitude 50 N. Avoid very popular regions like Valles Marineris and Gale crater, to get an image this semester. Floor of Hellas basin is often hazy, best to avoid in the current season. South Polar region is easy to image because the near-polar orbits converge.
  Put “Mars Class” in special notes box
  Look at past image suggestions to get an idea of what a good science rationale is like. First, go to https://hireport.lpl.arizona.edu/hireport/hi
      username: MarsClass
      password: MarsClass2015
    Examples of good science rationales:
    152206, 153680, 140102, 145678, 154858, 154968, 154856, 141874, 123642, 142142, 152228, 53390, 150654, 149620, 121478, 111600, 154640, 154602, 144464, 153962, 133902, 155002, 154256, 154394, 144042, 73304, 125498, 153868, 152802, 91848, 132934, 71746, 149254, 152960, 152874, 149670, 138184, 146154, 140636, 121312

## Slide 59: Always Examine HiRISE Images at Full resolution
If you just look at the browse products that are easy to see in HiReport, you are missing the unique capability of HiRISE.
These are large images, and we use JPEG2000 compression to enable rapid browse and zoom
Go to : https://www.uahirise.org/hiview/
  Download HiView tool, read the instructions
  There are alternatives if you can first download these large images, such as ENVI, Photoshop (if you have JPEG2000 enabled), Expressview, Preview (on Macs)
JMARS (https://jmars.asu.edu/) is a great Mars analysis tool, and can also render HiRISE images at full resolution
  To be demonstrated later